## Slide 1: SIGHT CubeSat
Team-15
Department of Space Science and Engineering (DSSE), NCU, Taiwan
Chen, Han-Kun Su, Yin-Rui Kuan, Ching-Jui

## Slide 2
Table of contents
Mission Definition & System Architecture
STR & EPS
Payload & GPS
01
02
03
04
OBC

## Slide 3: Mission Definition & System Architecture 01

## Slide 4: Team members
Su, Yin-Rui
OBC/Payload
Chen, Han-Kun PM/STR/EPS
Kuan, Ching-Jui
OBC/GPS

## Slide 5: Mission Definition
Cultivate students' independent research and development ability
Measuring tropospheric science data
Verification technology and components

## Slide 6: System Architecture
SIGHT CubeSat
STR
EPS
18650 battery
TP4056
OBC
Raspberry Pi
GPS 2
Payload
BMP280
DHT22
GL300
NEO 6M
Pi Camera
MPU6050

## Slide 7: STR & EPS 02

## Slide 8: STR
Introduction
Al 6061 material
Manufactured by German Datron NEO+ digital processing machine
Fusion 360 modeling, tool path design

## Slide 10: EPS
Introduction
18650 battery+TP4056
Hand-made power distribution board with PCB board
Supply power to whole satellite

## Slide 11: Payload & GPS 03

## Slide 12: Payload-MPU6050
Introduction
Measures three-axis acceleration and angular velocity data.

## Slide 13: Payload-MPU6050
Data processing
Obtain the CubeSat's three-axis attitude angles over time.

## Slide 14: Payload-MPU6050
Comparison
X axis accelerometer comparison
Y axis accelerometer comparison
Z axis accelerometer comparison

## Slide 15: Payload-BMP280
Introduction
Measures barometric pressure and temperature data, and calculates relative altitude changes based on pressure variations.

## Slide 16: Payload-DHT22
Introduction
Measures temperature and humidity data.

## Slide 17: Payload-Pi Camera
Introduction
The Pi Camera will record external images during satellite flight, , with each image lasting for one minute.
Camera Resolution: 1920*1080
camera.resolution = (1280,720)
#camera.rotation = 180
# delete exist video
video_file = 'video'+str(i)+'.h264'
if os.path.exists(video_file):
renamed_file = 'video'+str(i)+'.old'
os.remove(video_file, renamed_file)
# save to file(video)
camera.start_recording('/home/user/video'+str(i)+'.h264')
time.sleep(60)
camera.stop_recording()

## Slide 18: Payload-NEO-6m GPS Tracker (GPS1)
Introduction
This module will provide real-time satellite location information and assist us in retrieving the SD card after the satellite lands.

## Slide 19: OBC 04

## Slide 20: On-board computer
Introduction
Consists of two parts, Raspberry Pi 3 Model A+ and Raspberry Pi Zero 2W.
Raspberry Pi 3 Model A+ capturing images using the Raspberry Pi Camera
Raspberry Pi Zero 2W handles other sensors

## Slide 21: On-board computer
Program
On the Raspberry Pi Zero 2W, three programs will be automatically executed:
gpspress_print.py: Reads GPS longitude, latitude, and altitude, along with barometric, temperature and humidity data.
gpsprint.py: Only reads GPS longitude and latitude in case altitude data is missing.
mpu6050_raw.py: Reads three-axis acceleration and angular velocity data.
On the Raspberry Pi 3 Model A+, the program "camera.py" will be automatically executed.
camera.py: Record videos after startup, until the satellite loses power, and it will save a file every minute

## Slide 22: On-board computer
Data Processing
NEO-6m GPS data
Bmp280 data
Mpu6050 data

## Slide 23: On-board computer
Data Processing
GPS mapping

## Slide 24
Thank for listening
感謝聆聽